## Slide 1: DETR Model Improvements ECE508-02
By: Michael Schmidt
(A20460468)

## Slide 2: Table Of Contents
Introduction (Objective)
Evaluation
Conclusion
Baseline Model
Improvements Made

## Slide 3: Introduction

## Slide 4: Introduction
Objective:
  Improve the performance of DETR model:
    Improve Detection Accuracy
    Improve Training efficiency
    Improve Computational Complexity
Methods of Evaluations:
  Training speed
  IoU metrics
  Inference Speed
  #Params
Improve Training
Improve Detection
Improve Computation

## Slide 5: Introduction
Hyperparam Limits:
  LR = 5e-5
  Weight decay = 1e-4
  Epochs = 10
  Batch size = 4
Training Data:
Custom PASCAL VOC
20 Classes (Aeroplane, bird, cat, etc)
5717 training images
5823 testing
Training time: ~160 minutes
Accuracy = 60%
Avg Inference time = 0.0844
#Params = 41,506,778

## Slide 6: Baseline Model (DETR)

## Slide 7: Baseline Model (DETR)
CNN Backbone
(Feature Extraction)
Transformer Encoder-Decoder
(Self-Attention, Object queries, FFN, etc)
Prediction + Hungarian Matching
Source:
N. Carion, F. Massa, G. Synnaeve, N. Usunier, A. Kirillov, and S. Zagoruyko,
“End-to-End Object Detection with Transformers,” arXiv preprint arXiv:2005.12872, 2020.

## Slide 8: Baseline Model (DETR)
Source:
N. Carion, F. Massa, G. Synnaeve, N. Usunier, A. Kirillov, and S. Zagoruyko,
“End-to-End Object Detection with Transformers,” arXiv preprint arXiv:2005.12872, 2020.
Positional Sinusoids for PE
Flattens Features
6 layers:
Multi-head self attention
FFN
100 object queries
6 layers:
MHSA among queries
Cross-attention
FFN
Matching trains queries:
Should be object here
Should stay quiet

## Slide 9: Baseline Model (DETR)
Source:
N. Carion, F. Massa, G. Synnaeve, N. Usunier, A. Kirillov, and S. Zagoruyko,
“End-to-End Object Detection with Transformers,” arXiv preprint arXiv:2005.12872, 2020.
Visualization of 20 out of 100 predictions on COCO 2017 val set:
Each box represents what a query sees for BB
Points are center point of each BB
Green is small boxes
Red Large horizontal boxes
Blue large vertical boxes

## Slide 10: Improvements MAde

## Slide 11: Improvement #1 (Improve Accuracy)
Problem:
DETR is slow to converge
Solution:
Implement Denoising strategies
Speeds up convergence
Query predictions stabilize faster
Improved accuracy with little overhead
Source:
F. Li, H. Zhang, S. Liu, J. Guo, L. M. Ni, and L. Zhang, “DN-DETR: Accelerate DETR Training by Introducing Query DeNoising,” arXiv:2203.01305, 2022.

## Slide 12: Improvement #1 (Improve Accuracy)
How it works:
Adds new “Denoising queries” to the decoder
Gives model “easy training examples” early on
Creates two groups per image
  Positive examples: GT label + slightly perturb BB
  Negative examples: wrong labels + corrupt BB
No matching, assignments are fixed
Since assignments are fixed, loss calculations are only:
L1 loss between GT BB and pred BB
GIoU loss
Cross-entrophy for correct class
Source:
F. Li, H. Zhang, S. Liu, J. Guo, L. M. Ni, and L. Zhang, “DN-DETR: Accelerate DETR Training by Introducing Query DeNoising,” arXiv:2203.01305, 2022.

## Slide 13: Improvement #1 (Improve Accuracy)
Calculating Noise for DN examples
For Positive examples
  Labels stay the same
  Use BB corruption
For Negative Examples
  Label is corrupt
  Use BB corruption
Source:
F. Li, H. Zhang, S. Liu, J. Guo, L. M. Ni, and L. Zhang, “DN-DETR: Accelerate DETR Training by Introducing Query DeNoising,” arXiv:2203.01305, 2022.

## Slide 14: Improvement #1 (Improve Accuracy)
Hyperparams Used:
num_dn_groups = 5
Label_noise_ratio = 0.2
Box_noise_scale= 0.4
Training Time = ~170 minutes
Accuracy = 61.5%
Avg Inference Time = 0.0843s
#Params = 41,645,018
Source:
F. Li, H. Zhang, S. Liu, J. Guo, L. M. Ni, and L. Zhang, “DN-DETR: Accelerate DETR Training by Introducing Query DeNoising,” arXiv:2203.01305, 2022.

## Slide 15: Improvement #2 (Improve Computation + Inference)
Problem:
Decoder layers take time and recourses
  Computed self and cross attention
  Main bottleneck
Deep decoders have object queries communicate too much:
  causes over-correlation
  removing specialization
Solution:
Reduce decoder layer to 4
  Reduces FLOPs and memory
  Reduces over-correlation
  Very little accuracy loss
Source:
Z. Yao, Y. Ai, L. Gao, and B. Li, “Efficient DETR: Improving End-to-End Object Detector with Dense Prior,” arXiv:2104.01318, 2021.

## Slide 16: Improvement #2 (Improve Computation + Inference)
Hyperparams Used:
num_dn_groups = 5
Label_noise_ratio = 0.2
Box_noise_scale= 0.4
dec_layers = 4
Training Time = ~160 minutes
Accuracy = 61%
Avg Inference Time = 0.0832s
#Params = 38,487,514
Source:
Z. Yao, Y. Ai, L. Gao, and B. Li, “Efficient DETR: Improving End-to-End Object Detector with Dense Prior,” arXiv:2104.01318, 2021.

## Slide 17: Improvement #3 (Improve Computation + Inference)
Problem:
Each query detect an object + location
Cross attention scales with # of queries
100 queries can be redundant on dataset of 20 classes
Solution:
Reduce # queries to 50
  Force specialization
  Reduce redundant computations
Source:
Z. Xu, S. Wang, H. Yu, and G. Zhang, “DQ-DETR: DETR with Dynamic Query for Tiny Object Detection,” arXiv:2404.03507, 2024.
*Note: Even though source paper reduces #queries for each image, the idea and evidence of reduced queries was inspired by that paper

## Slide 18: Improvement #3 (Improve Computation + Inference)
Hyperparams Used:
num_dn_groups = 5
Label_noise_ratio = 0.2
Box_noise_scale= 0.4
dec_layers = 4
num_queries = 50
resize_queries
Training Time = ~160 minutes
Accuracy = 60.9%
Avg Inference Time = 0.0828s
#Params = 38,474,714
Source:
Z. Xu, S. Wang, H. Yu, and G. Zhang, “DQ-DETR: DETR with Dynamic Query for Tiny Object Detection,” arXiv:2404.03507, 2024.

## Slide 19: Improvement #4 (Improve Computation + Inference)
Problem:
Normal training uses FP32 for everything
FP32 is slow and heavy to compute
Solution:
Use Automatic Mixed Precision Training
  Automatically used FP16 where it is safe to avoid computational errors
  Improved training speed and mess memory with no accuracy loss
Source:
F. Li, H. Zhang, S. Liu, J. Guo, L. M. Ni, and L. Zhang, “DN-DETR: Accelerate DETR Training by Introducing Query DeNoising,” arXiv:2203.01305, 2022.

## Slide 20: Improvement #4 (Improve Computation + Inference)
How its implemented:
Source:
F. Li, H. Zhang, S. Liu, J. Guo, L. M. Ni, and L. Zhang, “DN-DETR: Accelerate DETR Training by Introducing Query DeNoising,” arXiv:2203.01305, 2022.
engine.py

## Slide 21: Improvement #4 (Improve Computation + Inference)
Hyperparams Used:
num_dn_groups = 5
Label_noise_ratio = 0.2
Box_noise_scale= 0.4
dec_layers = 4
num_queries = 50
resize_queries
amp
Training Time = ~110 minutes
Accuracy = 60.8%
Avg Inference Time = 0.0582s
#Params = 38,474,714
Source:
F. Li, H. Zhang, S. Liu, J. Guo, L. M. Ni, and L. Zhang, “DN-DETR: Accelerate DETR Training by Introducing Query DeNoising,” arXiv:2203.01305, 2022.

## Slide 22: Evaluation

## Slide 23: Evaluation
Default DETR Model
  Training time: ~160 minutes
  Accuracy = 60%
  Avg Inference time = 0.0844 ~11.8fps
  #Params = 41,506,778
DN-DETR + 4 Dec layers + 50 queries + AMP
  Training Time = ~110 minutes
  Accuracy = 60.8%
  Avg Inference Time = 0.0582s ~17fps
  #Params = 38,474,714

## Slide 24: Evaluation

## Slide 25: Evaluation

## Slide 26: Conclusion

## Slide 27: Conclusion
DN-DETR
Lower Decoder Layers + 50 Queries
Automatic Mixed Precision

## Slide 28: Thank You